## Slide 1: PINT: Probabilistic In-band Network Telemetry
Ran Ben Basat, Harvard University
Joint work with Sivaram Ramanathan, Yuliang Li (Harvard), Gianni Antichi (QMUL), Minlan Yu, Michael Mitzenmacher (Harvard)
1
Notes: Hi Everyone, thanks for joining.
Today I’ll be presenting our probabilistic approach for in-band network telemetry.
And this work is really enabled by this new trend of programmable network components we are now seeing

## Slide 2: The rise of programmable devices
2
Notes: We have now programmable switches and smartnics from many different vendors,

## Slide 3
3
Programmable Data Planes: not an academic dream
Notes: But this is not just an academic game, we now have smartnics deployed in the public cloud

## Slide 4: Killer App: Network Telemetry
4
Tell me more about my packets.
  Is there a congestion/queue buildup?
  Do routing paths agree with the policy?
  Can flow increase its sending rate?
Notes: So, one of the selling point for these switches is the new and exciting telemetry capabilities.
And telemetry is about knowing my network status.
For example, we want to know if there’s a queue buildup somewhere that is causing congestion, if all routes agree with the policy (e.g., we may want all flows to go through a firewall), and we can even use telemetry to know whether a flow can safely increase its sending rate without causing congestion at any point.

## Slide 5: INT: In-band Network Telemetry
Add hop information (e.g., switch ID) onto the packet
INT metadata value
INT header
INT
Packet
Header
Packet Payload
INT Source
5
INT
INT header
INT metadata value
Packet Payload
Packet
Header
INT
Packet Payload
Packet
Header
INT
INT header
INT metadata value
Packet Payload
Packet
Header
INT header
INT metadata value
Notes: To that end, we have the INT, or In-band Network Telemetry, protocol.
The idea is conceptually simple. If we want to collect date from the network, we can just add it to data packets.
For example, say that we want to discover the path taken by a flow, i.e., collect the switch IDs along the path.
In this case, the first participating hop (which can be either the end host or an ingress switch), which is also called the INT source, adds a new INT header that tells all switches along the path which information we are collecting (i.e., the switch ID). It then adds its own ID, and send the packet to the next hop.

## Slide 6: INT: In-band Network Telemetry
Add hop information (e.g., switch ID) onto the packet
INT metadata value
INT header
INT
Packet
Header
Packet Payload
INT Source
6
INT
INT header
INT metadata value
Packet Payload
Packet
Header
INT
INT header
INT metadata value
Packet Payload
Packet
Header
INT
Packet Payload
Packet
Header
INT header
INT metadata value

## Slide 7: INT: In-band Network Telemetry
Add hop information (e.g., switch ID) onto the packet
INT metadata value
INT header
INT
Packet
Header
Packet Payload
INT Source
7
INT
INT header
INT metadata value
Packet Payload
Packet
Header
INT
INT header
INT metadata value
Packet Payload
Packet
Header
INT
Packet Payload
Packet
Header
INT header
INT metadata value
INT
Packet Payload
Packet
Header
INT header
INT metadata value
INT header
INT metadata value
Notes: The next hop reads the INT header, figures out we are collecting switch IDs, adds its own and forwards the packet.

## Slide 8: Telemetry Use case #1 – Congestion Control
State of the art: High Performance Congestion Control (HPCC, SIGCOMM 2019) is deployed in production in Alibaba.
8

## Slide 9: Telemetry Use case #2 – Path Discovery
Which path do my packets take?
Which rules do my packets follow?
Does the path conform with the operator’s policy?
9
Barefoot
Advanced Network Telemetry

## Slide 10: Telemetry Use case #3 – Network Debugging
Identify switches/links with high latency.
Discover load imbalance.
10

## Slide 11: INT: In-band Network Telemetry
INT is general
  Supports a large variety of functions including latency and buffer measurements.
  INT is deployed in major companies such as Alibaba in production.
But introduces high packet overheads.
  A single function (e.g., switch ID), adds 4 bytes per hop.
  Overhead grows multilinearly with the path length and number of collected telemetry types.
11
Notes: Add company icons
Discuss use cases here

## Slide 12: INT: In-band Network Telemetry
Issue III: High packet overheads degrade application performance.
12
Packet Payload
Packet
Header
INT
Packet Payload
Packet
Header
Without INT
With INT
Notes: Add company icons
Discuss use cases here

## Slide 13: INT Drawbacks
Issue III: High packet overheads degrade application performance.
13
Path Tracing
HPCC
Both
Notes: 5-hop, fat tree, 64 hosts, web search workload, all are standard

## Slide 14: INT Drawbacks
Issue III: High packet overheads degrade application performance.
Issue III: High packet overheads increase switch processing time.
Issue III: High packet overheads
14
I
Approximately 1% increase per telemetry type on 10G link
Payload
Payload
INT
Notes: Add company icons
Discuss use cases here

## Slide 15: INT Drawbacks
Issue III: High packet overheads impose severe collection costs.
Issue III: High packet overheads increase switch processing time.
  High network overheads.
  High processing overheads.
  State of the art telemetry processing (e.g., Confluo, NSDI 2019) rely on fixed byte-size data and are incompatible.
Issue III: High packet overheads
15
I
Notes: Add company icons
Discuss use cases here

## Slide 16: PINT: Probabilistic In-band Network Telemetry
Goal: encode telemetry information on packets while minimizing the bit-overhead.
Values: when a packet reaches switch , the switch observes a value .
Insight: most applications do not need all per-packet per-switch values, but aggregated data.
Implementation: P4 code.
16

## Slide 17: PINT: Probabilistic In-band Network Telemetry
Per-packet aggregation:
  For each , aggregate (e.g., max/min/sum/product) the values along its path.
Per-flow aggregation: For a flow with packets
  Static Case
  Dynamic Case: for each switch on the path, aggregate (e.g., estimate the median) over
17
: compute for each switch on the path.
Packets
Switches
Output
Per-packet
Output
Static Per-flow
Dynamic Per-flow
Notes: Visualize

## Slide 18: Techniques
Global hash functions allow implicit switch agreement, e.g., on the query type.
Approximations can reduce bit-overhead for numerical values.
Coding helps reduce spreading out static information on multiple packets.
18

## Slide 19: PINT solves the overhead issues
The lower overhead reduces the goodput degradation significantly.
By lowering the packet overhead, PINT reduces the switch processing time.
PINT produces less information with fixed-size packet digests and reduces the collection overheads.
19
Notes: Visualize

## Slide 20: Use case 1: Congestion Control (per-packet aggregation)
Alibaba’s HPCC uses INT to collect latency and queue information to determine the sending rate.
The relevant quantity can be expressed as a MAX over a value that is approximated at switches for each packet.
20
Notes: 10% between each consecutive ticks

## Slide 21: Use case 2: Path Discovery (static per-flow aggregation)
Baseline solution: write a sampled ID on each packet.
  We can use the TTL field to get the hop number and run Reservoir Sampling (Sattari et al., 2010).
A
B
C
D
A Coupon Collector process. For hops it will take packets to detect the path.
C
A
A
D
A
C
B
21
Notes: RS allows us to get exact uniform distribution even though switches don’t know the path length
Static case is a generalization

## Slide 22: Coupon Collector Process
Number of samples
22
Notes: In some topologies, we may do better

## Slide 23: The power of Coding
23
A
B
The Baseline would:
Get information on the first packet.
Require 2 packets on average to get the second hop ID.
  Overall: packets in expectation.
Consider baseline sampling with probability 0.5, and writing otherwise.
If the first packet is an ID (e.g., ), we need more packets on average.
  Overall: packets in expectation.
𝐴⊕𝐵

## Slide 24: Path Profiling – the XOR algorithm
Assumptions:
  We know a “typical” length .
  Packets have unique identifiers.
Each switch XORs its identifier w.p. .
  Sample according to a global hash function
A
B
C
D
24

## Slide 25: Path Profiling – the XOR algorithm
Assumptions:
  We know a “typical” length .
  Packets have unique identifiers.
Each switch XORs its identifier w.p. .
  Sample according to a global hash function
A
B
C
D
25
Notes: ID can be 5-tuple / IPID / TCP seq / etc.

## Slide 26: Improving the Coupon Collector
26
Number of samples
Baseline
XOR
XOR

## Slide 27: Complete Algorithm
With probability , run the coupon collector algorithm.
Otherwise, choose one XOR layer at random.
The XOR instances have increasing probabilities.
Performance Guarantee: packets suffice.
Coupon collector
XOR1
XOR2
27
Notes: Add a results slide

## Slide 28: Also in the paper
Algorithms for dynamic aggregation.
Performance guarantees.
Support for concurrent queries.
28
Standalone
Concurrent
Standalone
Concurrent
Standalone
Concurrent